Advanced Battery Testing System

By all imagination, the Cadex C8000 may well be the most complete battery testing system available

| 4 independent digital drivers for maximum flexibility 1.2 – 36V, 10A charge and discharge per channel 100W per channel on charge; 80W on discharge | The Cadex C8000 stands in a class by itself in flexibility and affordable price. Test SMBus batteries, monitor cell balance and capture load signatures to observe batteries with a unique load protocol. Add a thermal chamber, external load bank, safety circuit and alarms to form a command center. |
| --- | --- |
| Digital Advantage Digital technology delivers a large test range and high power in a compact housing without the need to buy extra modules. Isolation is improved as neighboring channels do not interfere. Each of the four channels delivers 10A charge and discharge with a combined power of 400W on charge and 320W in discharge. | Algorithms include multiple safety redundancies. Identifies faulty battery and terminates service. |
|  | Monitoring individual cells Four differential (floating) analog inputs enable voltage check of up to 5 cells; 4 direct and one by voltage extraction. |

| Load Capture With the Load Capture Unit, the Cadex C8000 captures load signatures and plays them back as a simulated load protocol to check battery runtime in the lab. |  |
| --- | --- |
| External Load Bank For higher load current discharges, you can connect the C8000 to a designated external load bank, enabling loads of up to 2,400 watts and 48 volts. (Supported on one channel only). |  |
|  |  | Dual Power Port Cable The Dual Power Port Cable ties two channels together to double the current from 10A to up to 20A. (Discharge only) |
| Smart Battery Testing The Cadex C8000 reads the register settings of SMBus batteries to verify function use and identify anomalies. |  |
| Load test The Cadex C8000 tests batteries under GSM, DMA and other discharge protocols. Programming is in 50(s intervals with a minimum setting of 500(s. | Lifecycle test The program assists in battery selections and incoming inspections. The automated tests offer safety redundancy. |

| Cadex Electronics Inc. | ISO 9001 |
| --- | --- |
| 22000 Fraserwood Way, Richmond, BC, Canada V6W 1J6 Tel: 604 231-7777; 800 565-5228; Fax: 604 231-7755 | Farmstrasse 91-97, 64546 Moerfelden-Walldorf Germany Tel: +49 (0) 6105 975 11-0; Fax: +49 (0) 6105 975 11-29 |

info@cadex.com    www.cadex.com